ZARC Monitor Users’ Guide

Written by Merlin Skinner-Oakes, 8/5/2022
Last updated .
# Description
The Z80 Anachronistic Retro Computer (ZARC) monitor programme is an initial operating system for the ZARC computer. Features include:
- Memory examination and modification.
- Debugger.
- Serial port I/O drivers.
- Memory card sector read / write.
- Real time clock read and write.
- Utility routines.
- CP/M support.
In this document, the following style conventions are used:
Machine output
User commands
Comments
# Operating Principles
It is important to note that the monitor presents an environment in which the entire Z80 64 KB address space is addressable by the user. This allows debugging of the entire CP/M environment including BIOS and transient programmes, for example. The monitor is paged out of the memory map while the application programme is active.
Memory mapping should normally be enabled. If not, the application code will only have access to page 0x3f (the highest page). Write protection and supervisor are enabled. This page is used by the monitor, so great care is required to preserve the system. The command to enable memory mapping is:
set mmap 1
# Command Interface
Commands may be entered at the monitor command prompt "> ". The following control keys may be used:

Key	Function
DEL	Delete the character to the left of the cursor.
^P	Recall previous command in history.
^N	Recall next command in history.

The ^P and ^N history functions are similar to those implemented by most Linux / Unix shells. Commands may be abbreviated with '.', so the command:
disassemble
may be entered as any of the following, for example:
disassemble
disass.
dis.
di.
## Commands
### Help
Displays a summary of the available commands.
Syntax: help
### Dump
Display an area of memory in hex and ASCII.
Syntax: dump <start addr> [<length>]
<length> defaults to 0x0040 if not specified.
The format is similar to Linux's “hexdump -C”. Duplicate lines are omitted, and the omission is indicated by an ellipsis.
Example:
> dump 1000
1000 DA ED 09 23 18 F4 AF BE |...#....|
1008 C2 E4 09 CD FD 32 CD 5D |.....2.]|
1010 2A 2A 2A 2A 2A 2A 2A 2A |********|
        ...
1020 19 7E D3 07 E1 E5 7C E6 |.~....|.|
1028 3F C6 C0 67 CD 5D 18 77 |?..g.].w|
1030 E1 23 18 E0 CD 8C 1B DA |.#......|
1038 E4 09 78 A7 C2 E4 09 D5 |..x.....|
### Disassemble
Disassemble an area of memory.
Syntax: disassemble [<start addr>] [<length>]
<start addr> defaults to the current PC if not specified.
<length> defaults to 0x0010 if not specified.
Example:
> dis. ed30
ED30 31 2D F9 ld sp, 0xF92D
ED33 CD B8 F1 call 0xF1B8
ED36 AF xor a
ED37 32 03 00 ld (0x0003), a
ED3A 32 04 00 ld (0x0004), a
ED3D 3E 2C ld a, 0x2C
ED3F 32 5C F4 ld (0xF45C), a
## Read
Read a single memory location.
Syntax: read <addr>
Example:
> read ed30
31
## Write
Write data to memory.
Syntax: write <addr> <data1> [<data2> <data3> …]
Example:
> write 100 12 34 56 78
0004 bytes written
> dump 100 8
0100 12 34 56 78 F6 00 00 00 |.4Vx....|
## Fill
Fill a block of memory with a byte value.
Syntax: fill <addr> <length> <data>
Example:
> fill 100 8 2a
> dump 100 10
0100 2A 2A 2A 2A 2A 2A 2A 2A |********|
0108 00 00 00 00 00 00 00 00 |........|
## In
Read an I/O location.
Syntax: in <addr>
Example:
> in 1
08
## Out
Write data to I/O.
Syntax: out <addr> <data1> [<data2> <data3> …]
Example:
> out 11 2a
*0001 bytes written

Note: port 0x11 (IOA_SER1_DATA) is the data port for serial port 1. Writing “*” (ASCII 0x2a) to this address caused the “*” at the start of the line after the command.
## Map
Display or change the user context memory mapping.
Syntax: map [<bank> <page> [""prot""] [""super""]]
With no operands, the command displays the current state. To change the mapping, use: map <register> <page> [<prot>] [<super>]
Example:
> map 0 3f prot
> map 1 1
> map 2 2
> map 3 3
> map
0 (0000 - 3FFF): 3F [MONP] read only
1 (4000 - 7FFF): 01 [CPM1] writeable
2 (8000 - BFFF): 02 [CPM2] writeable
3 (C000 - FFFF): 03 [CPM3] writeable

Bank 0 is mapped to the monitor’s programme area, and is set to write-protected. The remaining banks are allocated to the CP/M system. Note that only the monitor’s pages are fixed. Use the “pages” command to find other allocations.
## Pages
Display page allocations.
Syntax: pages
Example:
> pages
Page Allocation Status:
0 - CPM0
1 - CPM1
2 - CPM2
3 - CPM3
62 - MOND
63 - MONP
58 pages free.
## Info
Display system information.
Syntax: info
Example:
> info
FPGA revision: 00.08
Total RAM: 1024 KB
CPU clock: 8004 KHz
Monitor starts: 6
Console port: ser1
Data transfer port: ser1
## MemTest
Test all of memory apart from the two pages used for the monitor. This is a very destructive test, and takes several minutes to execute. Use with caution!
Syntax: memtest
Example:
> memtest
Continue (y/n): y
Page 00
Pattern 00
Pattern FF
Pattern 01
Pattern 02
Pattern 04
Pattern 08
Pattern 10
Pattern 20
Pattern 40
Pattern 80
Pattern FE
Pattern FD
Pattern FB
Pattern F7
Pattern EF
Pattern DF
Pattern BF
Pattern 7F
Addressing test
Passed
Page 01
Pattern 00

…

Paging test
Passed

The output for only one page is shown for brevity.
## MonDownload
Runs code very similar to the stage 1 serial bootloader (the one normally entered from the front panel). This allows the monitor to be downloaded again.
Syntax: mondownload
This is a simple binary download, with all received characters being written to RAM starting at address zero. There is no form of checksum or other verification. Termination is by reset from the front panel. The only functional difference between this and the stage 1 bootloader is that this allows the use of either serial port. (see TPort command).
Example:
> mon.
Send binary data on port ser1. Press RESET to terminate.

Be careful not to send extraneous characters from the terminal before the intended data.
## BinDownload
Binary download from a serial port. This is useful for downloading raw binary files to the address specified. This is similar to the monitor download, but it allows an arbitrary address as destination in user address space. It is up to the user to make sure that the destination is writeable.
Syntax: bindownload <addr>
There is no form of checksum or other verification. Termination is by reset from the front panel.
Example:
> bin. 100
Send binary data on port ser1. Press RESET to terminate.
## TPADownload
Much as the bindownload command above, but downloads to the CP/M Transient Programme Area (TPA).
Syntax: tpadownload
Example:
> tpa.
Send binary data on port ser1. Press RESET to terminate.
## Time
Read from or write to the real time clock.
Syntax: time [<h>:<m>[:s>] [<d>/<m>/<y>]]
Example:
> time 11:38:00
11:38:0 Thursday 12/5/2022 BST
> time
11:38:5 Thursday 12/5/2022 BST
## Go
Call user code, using the current PC or a specified address.
Syntax: go [<addr>]
Example:
> go 100
## Trace / t
Call user code for one instruction (single step). If an address is specified, the trace is repeated until that address is reached. As this command is so often used during debugging, the command may be abbreviated to a single “t” with no full stop.
Syntax: trace | t [<addr>]
Example:
> set pc 100
> t

*** NMI (trace [single step]) ***
A: 07, F: (.Z.H...C), BC: 3E00, DE: 0000, HL: 1234
A': 3E, F': (S.....N.), BC': 2E20, DE': 0000, HL': C100
PC: 0103, SP: 41C1, IX: 4165, IY: 4408, I: FF, R: 22
IEn: 0, MMap: 00 [CPM0] , 01 [CPM1] , 02 [CPM2] , 03 [CPM3]
Stack: 0103 0302 0201 0103 0302 0201 0103 0302 0201 0103
 00FF 00 nop
 0100 21 34 12 ld hl, 0x1234
*0103 76 halt
 0104 03 inc bc
 0105 01 02 03 ld bc, 0x0302
## TraceOver / o
As trace, but if the current instruction is a CALL or RST, tracing continues until the call is complete. As this command is so often used during debugging, the command may be abbreviated to a single “o” with no full stop.
Syntax: traceover | o
Example:
> set pc 10d
> reg.
A: 00, F: (.Z.H.V..), BC: 015A, DE: E0F8, HL: 0175
A': 3E, F': (S.....N.), BC': 2E20, DE': 0000, HL': C100
PC: 010D, SP: 05F8, IX: 4165, IY: 4408, I: FF, R: 64
IEn: 0, MMap: 00 [CPM0] , 01 [CPM1] , 02 [CPM2] , 03 [CPM3]
Stack: 1A1A 1A1A 1A1A 1A1A 0201 0103 0302 0201 0103 0302
 0107 21 75 01 ld hl, 0x0175
 010A CD B3 02 call 0x02B3
*010D CD 5D 02 call 0x025D
 0110 30 09 jr nc, 0x011B
 0112 21 BF 01 ld hl, 0x01BF
> o

*** NMI (trace [single step]) ***
A: 43, F: (...H....), BC: 015A, DE: E0F8, HL: 0175
A': 3E, F': (S.....N.), BC': 2E20, DE': 0000, HL': C100
PC: 0110, SP: 05F8, IX: 4165, IY: 4408, I: FF, R: 4A
IEn: 0, MMap: 00 [CPM0] , 01 [CPM1] , 02 [CPM2] , 03 [CPM3]
Stack: 1A1A 1A1A 1A1A 1A1A 0201 0103 0302 0201 0103 0302
 010A CD B3 02 call 0x02B3
 010D CD 5D 02 call 0x025D
*0110 30 09 jr nc, 0x011B
 0112 21 BF 01 ld hl, 0x01BF
 0115 CD B3 02 call 0x02B3

In this example, the call at 0x10d is executed without without tracing each instruction with a separate “trace” command.
## Set
Set register to supplied value.
Syntax: set <reg> <value>
"ien" and "mmap" aren't actually registers, but are used here to control the interrupt enable and memory mapping respectively.
Example:
> set bc 5a5a
> reg.
A: 43, F: (...H....), BC: 5A5A, DE: E0F8, HL: 0175
A': 3E, F': (S.....N.), BC': 2E20, DE': 0000, HL': C100
PC: 0110, SP: 05F8, IX: 4165, IY: 4408, I: FF, R: 4A
IEn: 0, MMap: 00 [CPM0] , 01 [CPM1] , 02 [CPM2] , 03 [CPM3]
Stack: 1A1A 1A1A 1A1A 1A1A 0201 0103 0302 0201 0103 0302
 010A CD B3 02 call 0x02B3
 010D CD 5D 02 call 0x025D
*0110 30 09 jr nc, 0x011B
 0112 21 BF 01 ld hl, 0x01BF
 0115 CD B3 02 call 0x02B3
## Registers
Display register state. The instructions surrounding the PC are disassembled, which is very useful when tracing code.
Syntax: registers
Example:
> reg.
A: 43, F: (...H....), BC: 5A5A, DE: E0F8, HL: 0175
A': 3E, F': (S.....N.), BC': 2E20, DE': 0000, HL': C100
PC: 0110, SP: 05F8, IX: 4165, IY: 4408, I: FF, R: 4A
IEn: 0, MMap: 00 [CPM0] , 01 [CPM1] , 02 [CPM2] , 03 [CPM3]
Stack: 1A1A 1A1A 1A1A 1A1A 0201 0103 0302 0201 0103 0302
 010A CD B3 02 call 0x02B3
 010D CD 5D 02 call 0x025D
*0110 30 09 jr nc, 0x011B
 0112 21 BF 01 ld hl, 0x01BF
 0115 CD B3 02 call 0x02B3
## ReadSec
Read sectors from memory card.
Syntax: readsec <start sec> <no. of 512-byte sectors> <address>
<start sec> and <no. of 512-byte sectors> are decimal values.
Example:
> readsec 0 1 1000
Reading sector: 0
> dump 1180 80
1180 00 00 00 00 00 00 00 00 |........|
        ...
11B8 06 97 85 77 00 00 00 04 |...w....|
11C0 01 04 7F 47 02 48 00 08 |...G.H..|
11C8 00 00 00 88 00 00 00 00 |........|
11D0 00 00 00 00 00 00 00 00 |........|
        ...
11F8 00 00 00 00 00 00 55 AA |......U.|

In this example, the boot section is read. The dump shows the boot signature and partition entry no. 1.
## WriteSec
Write sectors to memory card.
Syntax: writesec <start sec> <no. of 512-byte sectors> <address>
<start sec> and <no. of 512-byte sectors> are decimal values.
Example:
> writesec 1 1 1000
Writing sector: 1
## Cache
Display memory card cache state.
Syntax: cache
Example:
MC Cache Status:
0 - 0 clean
1 - 1 dirty
2 - 4126 clean
3 - 4127 clean
4 - 4096 clean
5 - 4248 clean
6 - 4249 clean
7 - 4250 clean
8 - 4116 clean
9 - 4117 clean
10 - 4118 clean
11 - 4119 clean
12 - 4120 clean
13 - 4121 clean
14 - 4122 clean
15 - 4123 clean
In use: 16, dirty: 1, next read buffer: 2
## CPM
Load and start CP/M from the memory card.
Syntax: cpm [“debug"] ["noints"]
debug - enables BIOS debugging messages.
noints - disables interrupts (use basic I/O mode).
Example:
> cpm
ZARC CP/M V2.2 BIOS V1.1

A>
## CPort
Set console port. This defaults to ser1.
Syntax: cport <port>
<port> ::= "ser1" | "ser2"
Example:
> cport ser1
> info
FPGA revision: 00.08
Total RAM: 1024 KB
CPU clock: 8004 KHz
Monitor starts: 21
Console port: ser1
Data transfer port: ser1
## TPort
Set data transfer port. This defaults to ser1.
Syntax: tport <port>
<port> ::= "ser1" | "ser2"
Example:
> tport ser2
> info
FPGA revision: 00.08
Total RAM: 1024 KB
CPU clock: 8004 KHz
Monitor starts: 21
Console port: ser1
Data transfer port: ser2
## Cold
Perform a cold start. This reinitialises certain variables, such as the memory page allocations.
Syntax: cold
Example:
> cold

*** Cold start ***

____ __ ___ ___
   / / \ | \ /
  / |__| |__/ |
 / | | | \ |
/___ | | | | \___

ZARC Monitor V1.0
Initialising memory card
Product name: 000000
Serial number: B2000004
Manufactured: 12/2006
Total capacity: 31 MB
Block size: 512 bytes
> info
FPGA revision: 00.08
Total RAM: 1024 KB
CPU clock: 8004 KHz
Monitor starts: 1
Console port: ser1
Data transfer port: ser1
> pages
Page Allocation Status:
62 - MOND
63 - MONP
62 pages free.
# Operating Environment
This section describes some of the internal operation of the monitor and the environment it provides.
## Memory Map
The following page map is used by the monitor when it is active.
Bank Number	CPU Address Range	Mode	Function
0	0x0000 to 0x3fff	Read only, supervisor	Monitor programme
1	0x4000 to 0x7fff	Writeable	Monitor variables, stacks, buffers etc.
2	0x8000 to 0xbfff	As required	Mapped as required
3	0xc000 to 0xffff	As required	Mapped as required

Other pages are mapped into banks 2 and 3 as required. Page 0x3f is selected in hardware when memory mapping is not active, so on reset the monitor (page 0x3f at address 0) is entered. One of the monitor’s first tasks is to map banks 0 and 1 to establish its normal operating state.
## Externally Callable Functions
Many monitor function are made available to other applications. These have fixed entry points using a jump table in the same manner that CP/M uses. This allows changes to the monitor without having to recompile other modules. The jump vector table begins at location 0x0069 (immediately after the NMI vector). The table is defined in monitor.i. See CP/M BIOS for an example of use.
Use these routines with care. Consideration of memory paging, interrupts and stack location is required. When passing data by reference to its address, make sure the data is paged in and accessible to the routine.
A summary of the available functions follows:
Function	Source File	Function
MON_ENTRY	monitor.z80	Normal monitor entry
PANIC	monitor.z80	System error monitor entry
CONWCH	io.z80	Write character to the console port
CONRCH	io.z80	Read character from the console port
CONSTA	io.z80	Fetch console port status
S1WCH	io.z80	Write character to serial port 1
S1RCH	io.z80	Read character from serial port 1
S1STA	io.z80	Fetch serial port 1 status
S2WCH	io.z80	Write character to serial port 2
S2RCH	io.z80	Read character from serial port 2
S2STA	io.z80	Fetch serial port 2 status
CWNWLN	utility.z80	Write new line characters to console
CONWMS	utility.z80	Print null-terminated string to the console
CONWMN	utility.z80	Print message <n> in a list
SKPSPC	utility.z80	Step HL past spaces
TOUPCA	utility.z80	Convert character in A to upper case
TOLOCA	utility.z80	Convert character in A to lower case
CWVICH	utility.z80	Print only visible 7-bit characters
CWPSPC	utility.z80	Print a space
MTWDLI	utility.z80	Match word in a string against list of options
CWPHNB	utility.z80	Print least-significant nibble in A in hexadecimal
CWPHBY	utility.z80	Print A in hexadecimal
CWPHWD	utility.z80	Print HL in hexadecimal
CWPDBY	utility.z80	Print A in decimal. Leading zeros are suppressed.
CWPDWD	utility.z80	Print HL in decimal. Leading zeros are suppressed.
CWPDLO	utility.z80	Print DEHL in decimal. Leading zeros are suppressed
RDHXWD	utility.z80	Read a 16-bit hexadecimal number from a string
RDDUWD	utility.z80	Read a 16-bit unsigned decimal number from a string
RDDULO	utility.z80	Read a 32-bit unsigned decimal number from a string
MADLBU	maths.z80	32-bit / 8-bit unsigned divide
MADWBU	maths.z80	16-bit / 8-bit unsigned divide
MADBBU	maths.z80	8-bit / 8-bit unsigned divide
MAMWWU	maths.z80	16-bit * 16-bit unsigned multiply
MAMLBU	maths.z80	32-bit * 8-bit unsigned multiply
CRC16X	maths.z80	CRC-16 (XMODEM) – note that this is now replaced by hardware.
TIRD	time.z80	Read current time and date
TIWR	time.z80	Set time and date
TIITOS	time.z80	Convert integer time to structure
TISTOI	time.z80	Convert structure time to integer
CWPTM	time.z80	Print time structure to console
MCPRER	mmc.z80	Print memory card error text
CACRS	cache.z80	CP/M read sector
CACWS	cache.z80	CP/M write sector
CAFLUS	cache.z80	Flush cache (write dirty buffers)
MPALL	memory.z80	Allocate new page
MPFREE	memory.z80	Free allocated page
MPSTAT	memory.z80	Allocation status

See the relevant source files for full information. The terse function names are because the linker (ld80) only considers the first six characters of labels significant.
# Initial Boot
In normal use, the monitor is maintained by the battery backup mechanism and is started automatically when power is applied or on reset. If the monitor is not present or has become corrupt, it must be re-loaded. Hardware write protection and multiple sources of backup power make this a rare event.
The following short programme or equivalent must be entered from the front panel and executed. See ZARC HARDWARE USERS’ GUIDE for front panel operating instructions.

3FE0	3E 7F	LD a,0x7f	; Page 0x3f, SUPER=1 and PROT=0
3FE2	D3 04	OUT 0x04,a	; Page and prot. 0x0000-0x3fff
3FE4	3E 02	LD a,0x02
3FE6	D3 02	OUT 0x02,a	; Enable memory mapping
3FE8	0E 11	LD c,0x11	; Select console input port
3FEA	21 00 00	LD hl,0x0000	; Start address
3FED	LOOP:
3FED	ED A2	INI
3FEF	18 FC	JR loop	; Load data until reset
Initial Programme (Bootstrap)
This loads raw binary data from the serial port into memory starting at location zero. Press reset to stop the loader and run the newly downloaded code. Note that this transfer is pure binary data with no checksum. It is essential that the serial link is reliable to avoid data loss or corruption.
The monitor does not overwrite this boot loader, so if the monitor requires re-loading it should not be necessary to re-enter it.
# Example Session
This section demonstrates the entry and execution of a short programme. Comments are in blue.
Setup memory mapping.
> map 0 0	Map page 0 to bank 0
> set mmap 1	Ensure memory mapping is enabled
> map	Display mapping
0 (0000 - 3FFF): 00 [unallocated] writeable
1 (4000 - 7FFF): 01 [unallocated] writeable
2 (8000 - BFFF): 02 [unallocated] writeable
3 (C000 - FFFF): 03 [unallocated] writeable
Write programme to memory.
> write 0 0b 78 b1 20 fb 76
0006 bytes written
Disassemble it.
> dis. 0
0000 0B dec bc
0001 78 ld a, b
0002 B1 or c
0003 20 FB jr nz, 0x0000
0005 76 halt
0006 06 DE ld b, 0xDE
0008 03 inc bc
0009 01 02 03 ld bc, 0x0302
000C 01 02 03 ld bc, 0x0302
000F 01 02 03 ld bc, 0x0302
Set initial registers.
> set bc 0
> set pc 0
> set ien 0	Disable interrupts
> reg.	Display registers
A: 00, F: (........), BC: 0000, DE: 0000, HL: 0000
A': 00, F': (........), BC': 0000, DE': 0000, HL': 0000
PC: 0000, SP: 0000, IX: 0000, IY: 0000, I: 00, R: 00
IEn: 0, MMap: 00 [unallocated] , 01 [unallocated] , 02 [unallocated] , 03 [unallocated]
Stack: 780B 20B1 76FB DE06 0103 0302 0201 0103 0302 0201
*0000 0B dec bc
 0001 78 ld a, b
 0002 B1 or c
Trace a few instructions, one at a time.
> t

*** NMI (trace [single step]) ***
A: 00, F: (........), BC: FFFF, DE: 0000, HL: 0000
A': 00, F': (........), BC': 0000, DE': 0000, HL': 0000
PC: 0001, SP: 0000, IX: 0000, IY: 0000, I: 00, R: 4E
IEn: 0, MMap: 00 [unallocated] , 01 [unallocated] , 02 [unallocated] , 03 [unallocated]
Stack: 780B 20B1 76FB DE06 0103 0302 0201 0103 0302 0201
*0001 78 ld a, b
 0002 B1 or c
 0003 20 FB jr nz, 0x0000

ZARC Monitor V1.0
> t

*** NMI (trace [single step]) ***
A: FF, F: (........), BC: FFFF, DE: 0000, HL: 0000
A': 00, F': (........), BC': 0000, DE': 0000, HL': 0000
PC: 0002, SP: 0000, IX: 0000, IY: 0000, I: 00, R: 1C
IEn: 0, MMap: 00 [unallocated] , 01 [unallocated] , 02 [unallocated] , 03 [unallocated]
Stack: 780B 20B1 76FB DE06 0103 0302 0201 0103 0302 0201
*0002 B1 or c
 0003 20 FB jr nz, 0x0000
 0005 76 halt

ZARC Monitor V1.0
> t

*** NMI (trace [single step]) ***
A: FF, F: (S....V..), BC: FFFF, DE: 0000, HL: 0000
A': 00, F': (........), BC': 0000, DE': 0000, HL': 0000
PC: 0003, SP: 0000, IX: 0000, IY: 0000, I: 00, R: 6A
IEn: 0, MMap: 00 [unallocated] , 01 [unallocated] , 02 [unallocated] , 03 [unallocated]
Stack: 780B 20B1 76FB DE06 0103 0302 0201 0103 0302 0201
*0003 20 FB jr nz, 0x0000
 0005 76 halt
 0006 06 DE ld b, 0xDE

ZARC Monitor V1.0
Trace to address 5.
> t 5
This will take a very long time to complete as execution is slow when tracing. Pressing the NMI on the front panel results in a return to the monitor.

*** NMI (front panel) (trace [single step]) ***
A: 6D, F: (........), BC: 6824, DE: 0000, HL: 0000
A': 00, F': (........), BC': 0000, DE': 0000, HL': 0000
PC: 0001, SP: 0000, IX: 0000, IY: 0000, I: 00, R: 36
IEn: 0, MMap: 00 [unallocated] , 01 [unallocated] , 02 [unallocated] , 03 [unallocated]
Stack: 780B 20B1 76FB DE06 0103 0302 0201 0103 0302 0201
*0001 78 ld a, b
 0002 B1 or c
 0003 20 FB jr nz, 0x0000

ZARC Monitor V1.0
> set bc 100	Set a shorter delay
> t 5	Trace again
After a short delay, the machine halts (halt LED comes on). I pressed NMI to return to the monitor.

*** NMI (trace [single step]) ***
A: 00, F: (.Z...V..), BC: 0000, DE: 0000, HL: 0000
A': 00, F': (........), BC': 0000, DE': 0000, HL': 0000
PC: 0005, SP: 0000, IX: 0000, IY: 0000, I: 00, R: 20
IEn: 0, MMap: 00 [unallocated] , 01 [unallocated] , 02 [unallocated] , 03 [unallocated]
Stack: 780B 20B1 76FB DE06 0103 0302 0201 0103 0302 0201
*0005 76 halt
 0006 06 DE ld b, 0xDE
 0008 03 inc bc
Executing the programme directly (without tracing).

ZARC Monitor V1.0
> set pc 0
> go

After a short delay, the machine halts (halt LED comes on). I pressed RESET to return to the monitor.
____ __ ___ ___
   / / \ | \ /
  / |__| |__/ |
 / | | | \ |
/___ | | | | \___

ZARC Monitor V1.0
Initialising memory card
Product name: 000000
Serial number: B2000004
Manufactured: 12/2006
Total capacity: 31 MB
Block size: 512 bytes
>
# CP/M Debugging
This section describes use of the monitor’s debugger for use with CP/M. Much of this is also applicable to other operating systems and applications.
Start CP/M.

> cpm

ZARC CP/M V2.2 BIOS V1.5
A>

Start the application.

A> d:bitcoin

Press “NMI” on the front panel to enter the monitor.

*** NMI (front panel) ***
<register dump>

We can examine the code, make modifications and examine variables as required. Note that for programmes consisting of relocatable modules, it will be necessary to add the base address of the module from the .sym file to the address in the listing.

> dis. 100
0100 ED 73 4F 0F ld (0x0f4f), sp
0104 31 EC 0F ld sp, 0x0FEC
0107 CD 18 0B call 0x0B18
...

The trace (t) command is very useful when debugging. However, as this traces all instructions including interrupts, it is usually preferable to disable these to avoid unexpected jumps to interrupt service routines.

> set ien 0

Note that the BIOS will re-enable interrupts when they are required due to serial port access, so it may be necessary to disable them again.

> set pc 100

Now we can trace through the code.

> t

We might want to trace to a certain address, for example to just after the sign on message is printed. From the listing file:

0018' 219501 on_z80 ld hl, signon_msg
001B' CD0000 call conwms ; Print string
        ;
        ; Are we running on a ZARC system?
001E' CD0000 call zrcdet

This is part of bitcoin.z80, which is the first module loaded. From the .sym file we have:

Addr Length Typ Name Module File
=========================================
0100 0390 P - BITCOI bitcoin.rel

Hence the required address is 0x0100 + 0x001e = 0x011e.

> t 11e
*** Bitcoin Mining V1.0 ***

*** NMI (trace [single step]) ***
<register dump>

Control is returned to the monitor for further debugging commands. When the session is complete, the following command returns control to CP/M:

> go 0

This is a warm start, so any I/O redirection is preserved.