STran Users’ Guide

Serial file transfer for ZARC, but may have other applications.
Written by Merlin Skinner-Oakes, 14/3/2021
Last updated 25/10/2024 for stran V2.0

# Introduction
There are various options for transferring files over a serial line. The ZARC monitor’s tpadownload command works but is crude and manually entering the file length is prone to error. It also requires quite a bit of typing. Other options are gkermit and PCGET / PCPUT (Xmodem), but none seem to really do what I want them to do. Gkermit does work, but again is quite a bit of typing for each file. Scripts could ease this somewhat, but ideally I would like a single command from one end only that would transfer a file. It would be nice to be able to use wildcards or transfer an entire disk / directory as well.
# Architecture
The basic structure is:
1. A Python Linux program (“stran”) that would perform the PC side of the operation.
2. A CP/M program (also called stran) that would act as a server.
The Linux side controls the transfers. There are some advantages to having the Linux (rather than the CP/M) side control things:
1. Running the CP/M system with a single serial line and a terminal emulator on the PC is much simpler this way. Start the CP/M server using the terminal emulator, then exit and control things from the PC, optionally transferring data over the same line. Having the CP/M system in control would force the use of two serial lines, or one and a “built-in terminal” (display and keyboard).
2. This keeps the CP/M side simple. This is advantageous, as this will need to be written in assembler.
3. It will be easier to write scripts for operations such as drive backup in Python.
# Protocol
## Byte Encoding
ZARC serial ports are capable of full 8-bit operation with no special codes. However, some CP/M BIOS implementations remove bit 7, and other systems may use control codes such as XON and XOFF for special functions. For these reasons, a protocol that avoided use of control codes or bit 7 is preferred. Del (0x7f) is also avoided. Only codes 0x20 to 0x7e are used, with all but the packet start code (“*”) sent using codes 0x3f to 0x7e. The packet start code is chosen such that it cannot occur at any other point in a packet, thereby preventing byte synchronisation errors. Each three 8-bit bytes are encoded into four as follows:

Encoded Byte Number	Data
0	<byte 0 bits 7 to 2> + 0x3f
1	<byte 0 bits 1 to 0> <byte 1 bits 7 to 4> + 0x3f
2	<byte 1 bits 3 to 0> <byte 2 bits 7 to 6> + 0x3f
3	<byte 2 bits 5 to 0> + 0x3f

Zero padding is added as required to complete the four byte group when less than three bytes are to be sent at the end of a packet.
## Packet Format
Block length (BLKLEN) is fixed at 512 bytes. This was chosen to be shorter than that known to cause issues with at least some USB RS-232 adaptors (1024 bytes). Note that this length defines the maximum size of the data portion of the packet only. Allowance must also be made for the 3 to 4 bytes encoding scheme overhead.
In normal operation, transfers are in the form of packets with the following general format:
Start Offset	Data	Description
0	“*” (0x2a)	Start of packet (not encoded)
1	8 bits	Packet type (see below)
2	16 bits	Packet Sequence Number (“PSN”)
4	16 bits	Data length (0 to BLKLEN).
6	Data	Packet data (if present)
	0 to 16 bits	Padding to align to a 3-byte boundary.
	16 bits	CRC16 / XMODEM checksum of all fields except start of packet byte. Initial CRC is zero.
	8 bits	Pad to align to a 3-byte boundary.

The entire packet is encoded using the 3 to 4 bytes encoding scheme with exception of the initial “*”. 16-bit values are sent LS byte first.
## Packet Type Codes

Packet Type	Name	Source	Data Field Contents	Description
0x01	ACK	PC or CP/M	No data or one byte *2	Positive acknowledgement.
0x02	NAK	PC or CP/M	Reason for NAK (see below)	Negative acknowledgement.
0x03	Exit	PC	No data	Exit CP/M stran and return to CP/M.
0x04	Tx	PC	File descriptor block *1	Transmit file command (PC to CP/M).
0x05	Rx	PC	File descriptor block *1	Receive file command (CP/M to PC).
0x06	End	PC or CP/M	No data	Normal end of transfer.
0x07	Reset	PC	No data	Reset transfer system.
0x08	Dir	PC	Drive letter	Read directory.
0x09	Data	PC or CP/M	Data block

*1 <drive letter><8 character filename><3 character extension><Adler-32 checksum><CRC-16 (XMODEM)>.
*2 One data byte is sent in response to Tx or Rx commands. This reports whether or not the PC and CP/M files are identical. See Transfer Required Reason Codes below.
## NAK Reason Codes
These are sent as a single byte in the data field, so data length = 1.
Reason Code	Description
0x00	CRC error
0x01	Unexpected command
0x02	Can’t open file
0x03	BDOS file read / write error

## Transfer Required Reason Codes
These are sent as a single byte in the data field, so data length = 1.
Reason Code	Description
0x00	Files are identical (skip transfer)
0x01	Forced (CP/M /f command line option)
0x02	Bad file length
0x03	File lengths differ
0x04	Error calculating checksums
0x05	CRC does not match
0x06	Adler-32 does not match

## State Diagrams
These diagrams show the state transitions at the Linux end.
Blue “Transmit States” and “Receive States” invoke the state sequences shown below.

CP/M to PC file transfers are not implemented yet.
# Serial Ports
The CP/M code is designed to be used under either CP/M 2.x or CP/M 3. It uses BIOS functions to access the serial ports. Data transfers may use either the console (CON:) or auxiliary (AUX:). Note that AUX: is called RDR: (input) and PUN: (output) on CP/M 2.2.
# ^C (Break) Behaviour
Control C (^C) on the console port may be used to exit CP/M stran. There is a catch with this, however. If running on CP/M 2.x without a ZARC BIOS and transferring data on the AUX: port, there is no way of checking whether or not a character is available before calling the read routine. In this case, stran will effectively lock up until a character arrives on the AUX: (data) port. Hence ^C will not work under such circumstances until a character arrives on the AUX port, thereby unlocking the system.
# CP/M Command Line
The CP/M side may be started with the command stran. Options are available:
Command	Description
stran /c	Use CON: (console port) for data transfers.
stran /a	Use AUX: port (RDR: and PUN: on CP/M 2.x) for data transfers.
stran /b	Show build information and exit
stran /v	Show verbose messages (mainly for debugging)

Options may be combined, for example:
stran /cv

If neither /c or /a is specified, stran will accept data on either port. This is referred to as automatic port selection. This will not work on CP/M 2.x unless a ZARC BIOS is in use. This is because on such systems, there is no way for applications to determine whether or not a character is available on the READER: port without committing to a read (the required AUXIST and AUXOST BIOS functions are not supported).
# Port Redirection
The CON: and AUX (RDR: and PUN:) ports may be redirected to various physical devices. The details differ between CP/M 2.x and CP/M 3.
## CP/M 2.x
Under CP/M 2.x, this is normally achieved using the IOBYTE mechanism. Not all BIOSes implement this, however. The mappings may be changed using the CP/M STAT command.
STAT DEV:

shows the current device mapping. See https://www.seasip.info/Cpm/iobyte.html for further information.
# CP/M 3
CP/M 3 does not use IOBYTE, but instead implements a more flexible system. See device command (CP/M 3 User's Guide) for details.